## Slide 1
K.S.RANGASAMY COLLEGE OF TECHNOLOGY
(Autonomous)
www.ksrct.ac.in
20.01.2026
Mr. S. Nithilan, IV-ECE
Ms. S. Monisa, II-ECE
Mr. T. P. Nishanth, II-ECE
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
AeroLinkers

## Slide 2: Components Selection
Hardware Component Selection
MCU (STM32U375RG)
Wi-Fi Module (nRF7002)
Audio Codec (SGTL5000)
Haptic Driver (DRV2603)
Display (1.69" IPS TFT) Capacitive Touch
IMU (LSM6DSOX)
Battery
(Li-Po 300mAh)
PMIC (nPM1300)

## Slide 3: GPIO Mapping

## Slide 4: Power Architecture & Boot Sequence
Start
PMIC
VBAT & VIN -> VSYS
LDO
MCU and Display
MCU Enable Vout-1 in PMIC
Audio
IMU
Haptic
MCU Enable Vout-2 in PMIC
Wi-Fi

## Slide 5: Power Consumption & Dissipation
​Operation (Approx. time) | PMIC & LDO​ | MCU​ | Wi-Fi | DISPLAY & Back Light (50% PWM)​ | IMU​ | AUDIO​ | HAPTIC (50% PWM)​ | TOTAL​
Boot​ing (5 Sec) | 0.823 ​ | 3​ | 180​ | 50​ | 0.55​ | 5​ | ​30 | 269.37​
Data Communication​ (1 Sec) | 0.823 ​ | 3​ | ​60 | 0​ | 0.55 | ​5 | 30​ | ​99.37
Rest ​Position​ | 0.823 ​ | ​3​ | ​60 | ​0 | 0.55 | ​0 | 0​ | ​94.37
Wake ​Position​ | 0.823 ​ | ​3​ | ​60 | 50​ | 0.55 | 0​ | ​0 | 114.37​
Docking​ | 0.823 ​ | ​3​ | ​60 | 0​ | 0.55 | ​0 | ​0 | 64.37​
Vibration​ (1 Sec) | 0.823 ​ | 3​ | 60​ | 50​ | 0.55​ | 0​ | 30​ | 144.37​
All values are in Milliampere (mA)

## Slide 6: Reset Scheme and Interrupt Mapping
Applications can be reset by User Action Button
Peripherals can be reset by MCU through its interface
User Button -> High Priority _ Level-1
Touch -> Level-2
Wi-Fi -> Level-3

## Slide 7: CPU Selection and Memory Requirement
Parameter | STM32U375RG | nRF5340 | CC3551E | STM32U5
MCU Type | ULP MCU | Radio-centric SoC | Wi-Fi MCU SoC | ULP MCU
Integrated Radio | None | BLE | Wi-Fi | None
Architecture Impact | Arm® Cortex®-M33 32-bit RISC core | Wireless SoC with two Arm® Cortex®-M33 | Arm® Cortex®-M33 | Arm® Cortex®-M33
Active Current | 16 µA/MHz | 55 µA | 48 µA | 16 µA
Deep Sleep Current | ~1.6 µA | 2.2 µA | 2.8 µA | 1.9 µA
Lead Time | 6–8 wks | 10–12 wks | 12–14 wks | 8–10 wks
Memory (ROM / RAM) | 1 MB (1024 KB) / 512 KB | 1 MB (1024 KB) / 512 KB | 1 MB (1024 KB) / 512 KB | 1 MB (1024 KB) / 512 KB

## Slide 8: IDE, OS, CLI & Device Driver
Zephyr RTOS preferred – Low Footprint and Power Consumption
Linux not preferred – No need of much application and user interface
Device Driver for all selected components are available in Zephyr support page
For Command Line Interface, SSH preferred
WolfSSH library available for establishing SSH in Zephyr

## Slide 9: Device Menu
MAIN DISPLAY
Information
(Home Page)
PNR / Booking Details
Flight Status
Boarding Call Alerts
Lounge Access, Location & availability (Extended Feature)
Language
Settings
Device & Notification Language
Voice
Language
Display
Settings
Brightness
Text Size
Always ON Display
Sound & Haptic Settings
Volume
Vibration
About Device
Device ID
Version

## Slide 10: Exploded View

## Slide 11: Thank You !